## Slide 1: Cell Saver
Sujata Walode, Tutor, MGM SBSA

## Slide 2: Cell saver
Cell saver, also known as an autotransfusion device or cell salvage machine, is a medical device used during surgeries to collect and process a patient's own blood that is lost during the procedure. The collected blood is then reinfused back into the patient, reducing the need for allogeneic (donor) blood transfusions and minimizing the risk of complications associated with blood loss.
Here's an overview of the cell saver techniques, equipment, procedure, and instruments used:
1. Equipment:
Suction System: A suction system is used to collect the blood lost during the surgery. This can be a part of the surgical equipment, such as a suction catheter, or a dedicated cell saver suction system.
Cell Salvage Machine: The cell saver machine processes and cleans the collected blood to remove impurities like debris, fat, and contaminants. It consists of the following components:

## Slide 3
  Reservoir: The container where the collected blood is temporarily stored.
  Washing System: This is responsible for processing and washing the collected blood to remove unwanted components.
  Centrifuge: The centrifuge is used to separate blood components based on their density. It separates red blood cells from other components.
  Saline Solution: A sterile saline solution is used to wash the collected blood and help remove unwanted substances.
Collection and Reinfusion System: These are sterile, closed-loop systems that transport the processed blood back to the patient. The collected blood is reinfused into the patient through a transfusion set.

## Slide 4: Procedure
The cell saver procedure typically involves the following steps:
Step 1: Collection: As the surgery progresses, the blood that is lost from the surgical site is suctioned into the cell salvage system. The collected blood is anticoagulated to prevent clotting during storage.
Step 2: Processing: The collected blood is processed in the cell salvage machine. The machine separates red blood cells from unwanted components like debris and fat, and washes the red blood cells with a sterile saline solution.
Step 3: Filtration: The processed blood is filtered to ensure it is free from any remaining debris or contaminants.
Step 4: Reinfusion: The processed and filtered blood is then ready for reinfusion. It is transferred to a sterile container and connected to the patient through a transfusion set. The blood is slowly reinfused back into the patient.

## Slide 5: Instruments
The main instrument used for cell saver procedures is the cell salvage machine itself, which includes the components mentioned earlier:
Suction system (e.g., suction catheter or dedicated suction device)
Cell salvage machine (with reservoir, washing system, centrifuge, and saline solution)
Collection and reinfusion system (closed-loop system with a transfusion set)
It's important to note that while cell saver techniques can significantly reduce the need for allogeneic blood transfusions, they may not be suitable for all surgeries or patients. The decision to use a cell saver depends on the specific circumstances of the surgery and the patient's medical condition. The procedure should always be performed by trained healthcare professionals in a sterile and controlled environment.